## Slide 1: ME 233 Advanced Control II Lecture 14 Deterministic Input/Output Approach to SISO Discrete Time Systems Pole Placement, Disturbance Rejection and Tracking Control
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAAAAA

## Slide 2: SISO ARMA models
SISO State space model
Where all inputs and outputs are scalars:
control input
output
state

## Slide 3: SISO transfer function
relative degree

## Slide 4: SISO transfer function
relative degree
U(z) control input
Y(z) output

## Slide 5: ARMA Models
Define:
the back-step operator such that
the polynomials
relative degree (pure time delay)

## Slide 6: Back-step operator
Relationship to Z-transform
Similarly,

## Slide 7: SISO ARMA models
Auto-Regressive
Moving Average

## Slide 8: SISO ARMA models with persistent disturbances
SISO ARMA model with disturbance
Where all inputs and outputs are scalars:
control input
persistent (deterministic) but unknown disturbance
output

## Slide 9: Deterministic SISO ARMA models
Where polynomials:
are co-prime and d is the known pure time delay

## Slide 10: Polynomials in q-1
Monic polynomial
constant coefficient is 1
leading coefficient is 1
monic

## Slide 11: Polynomials in q-1
whenever p satisfies A(p) = 0
Co-prime polynomials have no common roots
are co-prime if and only if
The polynomials

## Slide 12: Polynomials in q-1
Anti-Schur polynomials have all of their roots outside the unit circle
For example, if the polynomial
is anti-Schur, then |q-1| > 1 whenever A(q-1) = 0

## Slide 13: Polynomials in q-1
for all sequences that satisfy
is anti-Schur if and only if

## Slide 14: Factorization of the zero polynomial B(q-1)
Assume the m order zero polynomial has
mu zeros that we do not want to cancel.
its remaining ms zeros inside the unit circle; these are the zeros we will cancel

## Slide 15: Factorization of the zero polynomial B(q-1)
Assume the m order zero polynomial has
mu zeros that we do not want to cancel.
its remaining ms zeros inside the unit circle; these are the zeros we will cancel
is anti-Schur
has the zeros (in q) that we
do not want to cancel

## Slide 16: Example
*
*
*
*

## Slide 17: Example
*
*
*
*
Example
we could have chosen to cancel these 2

## Slide 18: Deterministic SISO ARMA models
The zero polynomial:
Without loss of generality, we will assume that

## Slide 19: Control Objectives
Pole Placement: The poles of the closed-loop system must be placed at specific locations in the complex plane.
Closed-loop polynomial:
Where:
cancelable plant zeros
anti-Schur polynomial of the form
chosen by the designer

## Slide 20: Control Objectives
Tracking: The output sequence must follow a reference sequence which is known
In general, yd(k) can be generated by a reference model of the form
The design of Am(q -1) and Bm(q -1) is not a part of this control design technique and these polynomials do not enter into the analysis
anti-Schur polynomial

## Slide 21: Control Objectives
2. Tracking: The output sequence must follow a reference sequence which is known
Reference model:
Where:
reference output sequence, which is known in advance (i.e. yd(k+L) is available at instance k for some L>d).
anti-Schur polynomial
polynomial
chosen by the designer

## Slide 22: Control Objectives
Disturbance rejection: The closed-loop system must reject a class of persistent disturbances
Disturbance model:
Where
is a known annihilating polynomial
with zeros on the unit circle
are co-prime

## Slide 23: Deterministic disturbance examples
a) Constant disturbance:
Then,
b) Sinusoidal disturbance of known frequency:
Then,

## Slide 24: Deterministic disturbance examples
c) Periodic disturbance of known period
Then,
In all of these three examples, the polynomial has its roots on the unit circle.

## Slide 25: Control Law
Feedback and feedforward actions:
Feedforward action
(a-causal)
reference output

## Slide 26: Closed-Loop TF from r(k) to y(k)
Closed-loop characteristic polynomial
)

## Slide 27: Closed-Loop TF from r(k) to y(k)
If we let have the special structure

## Slide 28: Closed-Loop TF from r(k) to y(k)
Closed-loop characteristic polynomial
Given Ac(q-1), we would like to find polynomials
R(q-1) and S(q-1) so that

## Slide 29: The Diophantine (Bezout) equation
Given the co-prime polynomials
  is order n and has constant term 1
  is order m
and a polynomial of order nc with constant term 1

## Slide 30: The Diophantine (Bezout) equation
We wish to find polynomials
that satisfy the Diophantine equation:
given
same order as

## Slide 31: The Diophantine (Bezout) equation
Expanding in terms of coefficients:
order
order
order

## Slide 32: The Diophantine (Bezout) equation
Expanding in terms of coefficients:
We obtain:
given on next slide

## Slide 33: The Diophantine (Bezout) equation
Where the matrix
is given by:

## Slide 34
columns
columns

## Slide 35
If ns = n - 1, then these rows of zeros will not be here

## Slide 36: The Diophantine (Bezout) equation
Theorem: D is nonsingular iff the polynomials
and are co-prime.
The solution to the Diophantine equation is:

## Slide 37: Example:
Let
Solve for
order nc = 2
order n = 2
order m = 2
order m = 2
order ns

## Slide 38: Example:
4 equations and 4 unknowns

## Slide 39: Example:
Solution:
Equating coefficients of powers of q-1

## Slide 40: Return to the Control Problem…
Feedback and feedforward actions:
Feedforward (a-causal)

## Slide 41: Feedback Controller
Diophantine equation: Obtain polynomials
that satisfy:
plant zeros
Plant poles
Closed-loop
poles
We will factor
out the
polynomial next

## Slide 42: Controller Diophantine equation
Factor out polynomial
Therefore, we want to find R’(q-1) and S(q-1) such that

## Slide 43: Feedback Controller
Diophantine equation: Obtain polynomials
which satisfy:
Unstable plant zeros
Plant poles
Disturbance annihilating polynomial
Closed-loop
poles without
cancelled zeros

## Slide 44: Use previous solution of the Diophantine equation

## Slide 45: Diophantine equation
Solution:
These are the controller parameters!

## Slide 46: Feedback Controller
where
If the degree of the disturbance annihilator polynomial, nd is large (e.g. N is large),
then nr and ns are also large
Then, the solution of the Diophantine equation may be ill conditioned.

## Slide 47: Example
Plant:
Disturbance:
Select closed-loop poles:
Zeros:

## Slide 48: Diophantine equation
Solution:

## Slide 49: Example
Control:

## Slide 50: Feedback Control Law
Feedback control action:

## Slide 51: Proof – block diagram algebra
The closed-loop dynamics is from r(k) and d(k) to y(k)

## Slide 52: Proof – block diagram algebra
The closed-loop dynamics from d(k) to y(k) ( r(k) = 0 )
Substitute:
pole-zero
cancellation
Diophantine equation
1

## Slide 53: Proof – block diagram algebra
The closed-loop dynamics from d(k) to y(k) ( r(k) = 0 )
pole-zero
cancellation
Diophantine equation
1

## Slide 54: Proof – block diagram algebra
The closed-loop dynamics from r(k) and d(k) to y(k)

## Slide 55: Proof – block diagram algebra
Substitute:
pole-zero
cancellation
Diophantine equation
1

## Slide 56: Proof – block diagram algebra
pole-zero
cancellation
Diophantine equation
1

## Slide 57: Example
Control:

## Slide 58: Example
Closed-loop dynamics:
Unit step response

## Slide 59: Feedback Control Law
The feedback control action:
Results in the following closed-loop input/output dynamics:
well-damped zeros

## Slide 60: Feedforward Control
Feedforward control objective is to make y(k) follow yd(k) as closely as possible.
how well the objective met depends on
whether the plant has unstable zeros or not
or
Goal:

## Slide 61: Feedforward Control Synthesis
closed loop dynamics
from r(k) to y(k)

## Slide 62: Feedforward control principle: plant inversion
unstable zeros
cannot be inverted
closed-loop pole
polynomial
(anti-Schur)
pure step delays
≈1
approximate inverse
we need to know yd(k+d)

## Slide 63: Perfect Tracking Feedforward Control
Perfect tracking can be achieved if all plant zeros are cancelable, e.g.
in this case

## Slide 64: Tracking with unstable zeros
When the plant has unstable zeros we need to find an approximate inverse

## Slide 65: A-causal Bounded-Input Bounded-Output (BIBO) realization of a purely unstable operator
Then we can interpret in two ways:
is causal but unstable
is a-causal but BIBO
Let
i.e. all zeros of are
outside the unit circle

## Slide 66: A-causal Bounded-Input Bounded-Output (BIBO) realization of a purely unstable operator
Example:
Using an infinite series expansion,
infinite dimensional a-causal operator
unstable causal operator

## Slide 67: A-causal BIBO realization of a purely unstable operator
Thus,
Can be realized either as:
(unstable)
or
(a-causal BIBO)

## Slide 68: A-causal BIBO approximation of a purely unstable operator
We will now describe two methods of approximating a
purely unstable operator:
1) Truncated a-casual series expansion:
Zero-phase error feedforward operator:
(developed by Prof. Tomizuka)
Not q-1

## Slide 69: Example: realizing
Let,
1) Truncated a-casual series expansion:
Zero-phase error feedforward operator:
Not q-1

## Slide 70: Zero-phase error tracking
One of the most popular feedforward techniques for systems with unstable zeros.
Define the zero-phase operator

## Slide 71: Zero-phase error transfer function
A-causal zero-phase transfer function:
Properties:
It has zero-phase, i.e.
It has unity dc gain, i.e.

## Slide 72: Example: realizing
Let,
Zero-phase feedforward:
Zero-phase transfer function:

## Slide 73: Sinusoidal zero-phase error tracking
If yd(k) is a sinusoidal, there will be no phase shift between yd(k) and y(k)

## Slide 74: Zero-phase error feedforward

## Slide 75: Zero-phase error feedforward
Closed-loop dynamics: