## Slide 1: ME 233 Advanced Control II Lecture 18 Stability Analysis Using The Hyperstability Theorem
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAA

## Slide 2: Adaptive Control
Basic Adaptive Control Principle
Controller parameters are not constant, rather, they are adjusted in an online fashion by a Parameter Adaptation Algorithm (PAA)
When is adaptive control used?
Plant parameters are unknown
Plant parameters are time varying

## Slide 3: Example of a system with varying parameters
Temperature control system

## Slide 4: Adaptive Control Classification
Continuous time VS discrete time
Direct VS indirect
MRAS VS STR

## Slide 5: Model Reference Adaptive Systems (MRAS)

## Slide 6: Self-Tuning Regulators (STR)
estimates

## Slide 7: Identification of a LTI system
PAA
Parallel model

## Slide 8: Identification of a LTI system
Parameter
Adaptation
Algorithm
Series-parallel model
regressor
(We will use this model throughout this lecture)

## Slide 9: Plant ARMA Model
Plant model
where

## Slide 10: Unknown plant parameters
Assume ARMA model parameters are unknown
As the unknown parameter vector
Define:

## Slide 11: Regressor vector
Collect all measurable signals in one vector
as the known regressor vector
We define

## Slide 12: Plant ARMA Model
Plant model
where

## Slide 13: Plant ARMA Model
Plant estimate (series-parallel)
where

## Slide 14: Plant output estimate
Plant a-posteriori estimate
Plant a-priori estimate

## Slide 15: Plant a-posteriori error
error:

## Slide 16: A Parameter Adaptation Algorithm
PAA
Parameter error update law:

## Slide 17: Adaptation Dynamics
a-posteriori error:
Parameter error update law:

## Slide 18: Adaptation Dynamics
PAA
PAA:

## Slide 19: Convergence of Adaptive Systems
Adaptive systems are nonlinear
We need to prove that the algorithms converge:
Output error convergence
Parameter error convergence

## Slide 20: Output error Convergence
Our first goal will be to prove the asymptotic convergence of the output error:
Two frequently used methods of stability analysis are:
Stability analysis using Lyapunov’s direct method
  State space approach
Stability analysis using the Passivity or Hyperstability theorems
  Input/output approach

## Slide 21: Hyperstability
Hyperstability Theory
Developed by V.M. Popov to analyze the stability of a class of feedback systems (monograph published in 1973)
Popularized by I.D. Landau for the analysis of adaptive systems (first book published in 1979)

## Slide 22: Hyperstability Theory
Hyperstability Theory
Applies to both continuous time and discrete time systems
Abuse of notation: We will denote the LTI block by its transfer function

## Slide 23: CT Hyperstability Theory
A state space description of the LTI Block:

## Slide 24: CT Hyperstability Theory
P-class nonlinearity: (passive nonlinearities)
Where is a constant which is a function of the
initial conditions

## Slide 25: CT Hyperstability Theory
Where is a constant which is a function of the
initial conditions
P-class
nonlinearity

## Slide 26: Example: Static P-class NL

## Slide 27: Example: Static P-class NL

## Slide 28: Example: Dynamic P-class block
P-NL

## Slide 29: Example: Dynamic P-class block

## Slide 30: Example: Passive mechanical system
Input is force and output is velocity
passive
mechanical
system
force
velocity

## Slide 31: Example: Passive mechanical system
Input is force and output is velocity
System Energy:

## Slide 32: Example: Passive mechanical system
Input is force and output is velocity
Differentiating energy

## Slide 33: Example: Passive mechanical system
Input is force and output is velocity
Differentiating energy
power input

## Slide 34: Example: Passive mechanical system
Input is force and output is velocity
integrating power,

## Slide 35: Examples of P-class NL
Lemma:
The parallel combination of two P-class nonlinearities is also a P-class nonlinearity.

## Slide 36: Examples of P-class NL
Lemma:
The feedback combination of two P-class nonlinearities is also a P-class nonlinearity.

## Slide 37: CT Hyperstability
Hyperstability: The above feedback system is hyperstable if there exist positive bounded constants such that, for any state space realization of G(s),
FOR ALL P-class nonlinearities

## Slide 38: CT Asymptotic Hyperstability
Asymptotic Hyperstability: The above feedback system is asymptotically hyperstable if
It is hyperstable
For all signals (I.e. bounded output of any P-class nonlinearity), and any state space realization of G(s),

## Slide 39: CT Hyperstability Theorems
Hyperstability Theorem: The above feedback system is hyperstable iff the transfer function G(s) of the LTI block is Positive Real.
Asymptotical Hyperstability Theorem: The above feedback system is asymptotically hyperstable iff the transfer function G(s) of the LTI block is Strictly Positive Real.

## Slide 40: CT Positive Real TF
Is Positive Real iff:
G(s) does not have any unstable poles (I.e. no Re{s} > 0).
Any pole of G(s) that is in the imaginary axis does not repeat and its associated residue (I.e. the coefficient appearing in the partial fraction expansion) is non-negative.
for all real w’s for which s = j w is not a pole of G(s)

## Slide 41: Strictly Positive Real (SPR) TF
Is Strictly Positive Real (SPR) iff:
All poles of G(s) are asymptotically stable.
2.
for all
Example:

## Slide 42: Strictly Positive Real (SPR) TF
For scalar rational transfer functions
All poles of G(s) are asymptotically stable.
2. for all
Note:
A necessary (but not sufficient)
condition for G(s) to be SPR is that
its relative degree must be less than or
equal to 1.

## Slide 43: Kalman Yakubovich Popov Lemma
Is Strictly Positive Real (SPR) if and only if
there exist a symmetric and positive definite matrix P,
matrices L and K,
and a constant ε > 0 such that

## Slide 44: Kalman Yakubovich Popov Lemma
Is Strictly Positive Real (SPR) iff there exist symmetric and positive definite matrices P and Q, such that:

## Slide 45: SPR TF implies Possitivity
Let be SPR
Then there exist positive definite functions
and a positive semi-definite function
Such that the input u(t) output y(t) pair satisfies

## Slide 46: SPR TF implies Passivity
Proof: We consider a strictly causal transfer function
which is SPR, with state space realization
By the Kalman Yakubovich, Popov lemma, there exist symmetric and positive definite matrices P and Q, such that

## Slide 47: SPR TF implies Passivity
Proof: Define the PD function
and compute:
by the Kalman Yakubovich, Popov lemma.

## Slide 48: SPR TF implies Passivity
Proof: Thus, since
Define the PD function and integrate

## Slide 49: DT Hyperstability Theory
State space description of the LTI Block:

## Slide 50: DT Hyperstability Theory
P-class nonlinearity: (passive nonlinearities)
Where is a bounded constant.

## Slide 51: Example: Static nonlinearity:
P-block

## Slide 52: Example: Dynamic P-class block
P-block

## Slide 53: Example: Dynamic P-class block

## Slide 54: Example: Dynamic P-class block

## Slide 55: Example: Dynamic P-class block
P-block

## Slide 56: Example: Dynamic P-class block
P-block

## Slide 57: Example: Dynamic P-class block

## Slide 58: Example: Dynamic P-class block

## Slide 59: Example: Dynamic P-class block
P-block

## Slide 60: Examples of P-class NL
Lemma:
The parallel combination of two P-class nonlinearities is also a P-class nonlinearity.
The feedback combination of two P-class nonlinearities is also a P-class nonlinearity.

## Slide 61: DT Hyperstability
Hyperstability: The above feedback system is hyperstable if there exist positive bounded constants such that,
for any state space realization of G(q),
FOR ALL P-class nonlinearities

## Slide 62: DT Asymptotic Hyperstability
Asymptotic Hyperstability: The above feedback system is asymptotically hyperstable if
It is hyperstable
for any state space realization of G(z),

## Slide 63: DT Hyperstability Theorems
Hyperstability Theorem: The above feedback system is hyperstable iff the transfer function G(z) of the LTI block is Positive Real.
Asymptotical Hyperstability Theorem: The above feedback system is asymptotically hyperstable iff the transfer function G(z) of the LTI block is Strictly Positive Real.

## Slide 64: Positive Real TF
Is Positive Real iff:
G(z) does not have any unstable poles (I.e. no |z| > 1).
Any pole of G(z) that is in the unit circle does not repeat and its associated residue (i.e. the coefficient appearing in the partial fraction expansion) is non-negative.
for all for which z = e j w is not a pole of G(z)

## Slide 65: Strictly Positive Real (SPR) TF
Is Strictly Positive Real (SPR) iff:
All poles of G(z) are asymptotically stable.
2.
for all
Example:

## Slide 66: Strictly Positive Real (SPR) TF
For scalar rational transfer functions
All poles of G(z) are asymptotically stable.
2. for all
Note:
A necessary (but not sufficient)
condition for G(z) to be SPR is that
its relative degree must be 0.

## Slide 67: Matrix Inequality Interpretation of SPR
The transfer function
is Strictly Positive Real (SPR) if and only if
there exists such that

## Slide 68: SPR state-space realization fact
Theorem: If G(z) = C(zI-A)-1B + D is SPR, then
Proof: Choose such that
Note that

## Slide 69: SPR TF is P-class
Let be SPR
Then there exist positive definite functions
Such that any input u(k) output y(k) pair satisfies

## Slide 70: Shorthand notation

## Slide 71: Proof
Let be SPR
Choose such that
Define the Lyapunov function
and the function

## Slide 72: Proof

## Slide 73: Proof
From the previous slide
Summing both sides of the equation yields

## Slide 74: Proof of the sufficiency part of the Asymptotic Hyperstability Theorem - Discrete Time
Since the nonlinearity is P-class,
Since LTI block is SPR, we can use the choose such that
SPR
P-class

## Slide 75: Hyperstability
SPR
From the previous proof (SPR TF is P-class), we have
where

## Slide 76
From the P-class nonlinearity:
SPR
Rearranging terms,
Hyperstability
Therefore,

## Slide 77
SPR
From the previous slide
Hyperstability
Therefore, the feedback system is hyperstable

## Slide 78: Asymptotic Hyperstability
SPR
monotonic nondecreasing sequence in k
bounded above
Therefore, the feedback system is asymtotically hyperstable

## Slide 79: Additional Result
SPR
Therefore, x(k), u(k), v(k), and w(k) converge to 0
We have already shown that
From this we see that

## Slide 80: Stability analysis of Series-parallel ID
Parameter
Adaptation
Algorithm
regressor

## Slide 81: Series-Parallel ID Dynamics (review)
a-posteriori error:
Parameter error update law:

## Slide 82: Series-Parallel ID Dynamics (review)
PAA
PAA:

## Slide 83: Stability analysis of Series-parallel ID
PAA
Strictly Positive Real

## Slide 84: Stability analysis of Series-parallel ID
PAA

## Slide 85: Stability analysis of Series-parallel ID
PAA
SPR
P-class
By the sufficiency portion of Hyperstability Theorem:

## Slide 86: Stability analysis of Series-parallel ID
PAA
SPR
P-class
By the sufficiency portion of Asymptotic Hyperstability Theorem:
Q.E.D.

## Slide 87: Stability analysis of Series-parallel ID
PAA
SPR
P-class
By the sufficiency portion of Asymptotic Hyperstability Theorem:

## Slide 88: How to we implement the PAA?
a-posteriori error & PAA:
Solution: Use the a-priori error
Static
coupling

## Slide 89: How to we implement the PAA?
a-posteriori estimate & PAA:
Solution: Use the a-priori error
Static
coupling

## Slide 90: How to we implement the PAA?
Multiply by
Therefore,

## Slide 91: How we implement the PAA

## Slide 92: Stability analysis of Series-parallel ID
Under the following assumptions:
is anti-Schur
We have shown that
Now we will show that
Since
Since
Parameter
Adaptation
Algorithm
regressor

## Slide 93: Stability analysis of Series-parallel ID
Thus, we know that
Remember that
Parameter
Adaptation
Algorithm
regressor

## Slide 94: Stability analysis of Series-parallel ID
What about the parameter error ?
We have shown that
since
However, this does not imply that the parameter error goes to zero
We need to impose another condition on u(k) to guarantee that the parameter error goes to zero. (persistence of excitation)
Parameter
Adaptation
Algorithm
regressor