## Slide 1: ME233 Advanced Control II Lecture 1 Dynamic Programming & Optimal Linear Quadratic Regulators (LQR)
(ME233 Class Notes DP1-DP4)
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAA

## Slide 2: Outline
Dynamic Programming
Simple multi-stage example
Solution of finite-horizon optimal
Linear Quadratic Reguator (LQR)

## Slide 3: Dynamic Programming
Invented by Richard Bellman in 1953
From IEEE History Center: Richard Bellman:
  “His invention of dynamic programming in 1953 was a major breakthrough in the theory of multistage decision processes…”
  “A breakthrough which set the stage for the application of functional equation techniques in a wide spectrum of fields…”
  “…extending far beyond the problem-areas which provided the initial motivation for his ideas.”

## Slide 4: Dynamic Programming
Invented by Richard Bellman in 1953
From IEEE History Center: Richard Bellman:
  In 1946 he entered Princeton as a graduate student at age 26.
  He completed his Ph.D. degree in a record time of three months.
  His Ph.D. thesis entitled “Stability Theory of Differential Equations" (1946) was subsequently published as a book in 1953, and is regarded as a classic in its field.

## Slide 5: Dynamic Programming
We will use dynamic programming to derive the solution of:
Discrete time LQR and related problems
Discrete time Linear Quadratic Gaussian (LQG) controller.
  Optimal estimation and regulation

## Slide 6: Dynamic Programming Example
Illustrative Example:
Find “optimal” path:
From A to B
by moving only to the right.
if we are here…
ok
ok
not ok

## Slide 7: Dynamic Programming Example
Illustrative Example:
Find “optimal” path:
From A to B
by moving only to the right.
Number next to line is the “cost” in going along that particular path.

## Slide 8: Dynamic Programming Example
7
Illustrative Example:
Find “optimal” path:
From A to B
by moving only to the right.
11

## Slide 9: Dynamic Programming Example
16
Illustrative Example:
Find “optimal” path:
From A to B
by moving only to the right.
23

## Slide 10: Dynamic Programming Example
Illustrative Example:
Find optimal path:
From A to B
by moving only to the right.
Optimal path from A to B is the one with the smallest overall cost.
There are 70 possible routes starting from A.

## Slide 11: Dynamic Programming
Key idea:
Convert a single “large” optimization problem into a series of “small” multistage optimization problems.
  Principle of optimality: “From any point on an optimal trajectory, the remaining trajectory is optimal for the corresponding problem initiated at that point.”
  Optimal Value Function: Compute the optimal value of the cost from each state to the final state.

## Slide 12: Dynamic Programming Example
Illustrative Example:
Use principle of optimality
Compute Optimal Value Function and optimal control at each state
Start from the final state B
9
12
7
11
assume that
we are here…
determine the
optimal path
from to B

## Slide 13: Dynamic Programming Example
Illustrative Example:
Use principle of optimality
Compute Optimal Value Function and optimal control at each state
Start from the final state B
9
12
7
11
two options:
7 + 9 = 16
11 + 12 = 23

## Slide 14: Dynamic Programming Example
Illustrative Example:
Use principle of optimality
Compute Optimal Value Function and optimal control at each state
Start from the final state B
9
12
Assign:
optimal path
optimal cost
16

## Slide 15: Dynamic Programming Example
Illustrative Example:
Use principle of optimality
Compute Optimal Value Function and optimal control at each state
Start from the final state B
9
12
Continue…
16
15
12
10
10 + 15 = 25
12 + 16 = 28

## Slide 16: Dynamic Programming Example
Illustrative Example:
Use principle of optimality
Compute Optimal Value Function and optimal control at each state
Start from the final state B
9
12
Continue…
16
15
10 + 15 = 25
12 + 16 = 28
25

## Slide 17: Dynamic Programming Example
Optimal cost:
Continue until
A is reached

## Slide 18: LTI Optimal regulators
State space description of a discrete time LTI
Find “optimal” control
That drives the state to the origin
For now, everything is deterministic
In some sense, to be defined later…

## Slide 19: Finite Horizon LQ optimal regulator
Consider the nth order discrete time LTI system:
We want to find the optimal control sequence:
which minimizes the cost functional:

## Slide 20: Finite Horizon LQ optimal regulator
Consider the nth order discrete time LTI system:
Notice that the value of the cost depends on the initial condition
To emphasize the dependence on

## Slide 21: LQ Cost Functional:
total number of steps—“horizon”
penalizes the final state deviation from the origin
penalizes the transient state deviation from the origin and the control effort
symmetric

## Slide 22: LQ Cost Functional:
Simplified nomenclature:
final state
cost
transient
cost at each
step

## Slide 23: Additional notation
For define:
Optimal control sequence from instance m
Arbitrary control sequence from instance m:

## Slide 24: Dynamic Programming
Optimal cost functional
Control sequence from instance 0
Function of initial state

## Slide 25: Optimal Incremental Cost Function
Optimal cost function from state x(m) at instant m
Control sequence from instance m
For define:

## Slide 26: Optimal Cost Function
Optimal cost function at the final state x(N)
… only a function of the final state x(N)

## Slide 27: Dynamic Programming
Optimal value function:
For :

## Slide 28: Dynamic Programming
Optimal value function:

## Slide 29: Dynamic Programming
Optimal value function:
given x(m), these are only functions of u(m) !!
only an optimization with respect to a single vector

## Slide 30: Bellman Equation
The Bellman equation can be solved recursively (backwards), starting from N:
Each iteration involves only an optimization with respect to a single variable (u(m)) – multistage optimization

## Slide 31: Recursive Solution to the Bellman Equation
known function of x(N)
not known
boundary condition

## Slide 32: Recursive Solution to the Bellman Equation
Start with N-1:
find by solving:
assume that x(N-1) is given
will be a function of
known function of

## Slide 33: Recursive Solution to the Bellman Equation
Continue with N-2:
find by solving:
assume that x(N-2) is given
will be a function of
known function of

## Slide 34: Solving the Bellman Equation for a LQR
1)
2)
Quadratic functions

## Slide 35: Minimization of quadratic functions
For we have that:
Optimal u given by
Proof:
Completing the square

## Slide 36: Minimization of quadratic functions
For we have that:
Optimal u given by
Proof:

## Slide 37: Finite-horizon LQR solution
Where P(k) is computed backwards in time using the
discrete Riccati difference equation :

## Slide 38: Proof of finite-horizon LQR solution
Proof (by induction on decreasing k)
Let
(Trivially holds for k=N -1 by definition of )

## Slide 39: Proof of finite-horizon LQR solution

## Slide 40: Proof of finite-horizon LQR solution
The Bellman equation gives

## Slide 41: Proof of finite-horizon LQR solution
Using results for quadratic optimizations:
where

## Slide 42: Example – Double Integrator
Double integrator with ZOH and sampling time T =1:
position
velocity

## Slide 43: Example – Double Integrator
Choose:
LQR cost:
only penalize
position x1
and control u

## Slide 44: Example – Double Integrator (DI)
Compute P(k) for an arbitrary and N.
Computing backwards:

## Slide 45: Example – DI Finite Horizon Case 1
N = 10 , R = 10,
P11(k)
P22(k)
P12(k)

## Slide 46: Example – DI Finite Horizon Case 2
N = 30 , R = 10,
P11(k)
P22(k)
P12(k)

## Slide 47: Example – DI Finite Horizon Case 3
N = 30 , R = 10,
P11(k)
P22(k)
P12(k)

## Slide 48: Example – DI Finite Horizon
Observation:
In all cases, regardless of the choice of
when the horizon, N, is sufficiently large
the backwards computation of the Riccati Eq.
always converges to the same solution:
We will return to this important idea in a few lectures

## Slide 49: Properties of Matrix P(k)
P(k) satisfies:
1)
2)
(symmetric)
(positive semi-definite)

## Slide 50: Properties of Matrix P(k)
(symmetric)
Proof: (by induction on decreasing k)
Base case, k=N :
For :
Transpose both sides of the equation

## Slide 51: Properties of Matrix P(k)
(positive semi-definite)
Proof: (by induction on decreasing k)
Base case, k=N :
For :
Algebra…

## Slide 52: Summary
Bellman’s dynamic programming invention was a major breakthrough in the theory of multistage decision processes and optimization
Key ideas
  Principle of optimality
  Computation of optimal cost function
Illustrated with a simple multi-stage example

## Slide 53: Summary
Bellman’s equation:
  has to be solved backwards in time
  may be difficult to solve
  the solution yields a feedback law

## Slide 54: Summary
Linear Quadratic Regulator (LQR)
Bellman’s equation is easily solved
Optimal cost is a quadratic function
matrix P is solved using a Riccati equation
Optimal control is a linear time varying feedback law