## Slide 1: ME 233 Advanced Control II Lecture 22 Indirect Adaptive Pole Placement, Disturbance Rejection and Tracking Control
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAA

## Slide 2: Adaptive Control
Adaptive Control Principle
Controller parameters are not constant, rather, they are adjusted in an online fashion by a Parameter Adaptation Algorithm (PAA)
When is adaptive control used?
Plant parameters are unknown
Plant parameters are slowly time varying

## Slide 3: Self-Tuning Regulator (STR):

## Slide 4: Self-tuning Regulator Approach
Control Design Procedure:
  Pole-placement, tracking control and deterministic disturbance rejection for ARMA models (Lecture 16).
Model Identification:
  Series-parallel with Recursive Least Squares (RLS) identification with or without forgetting factor.

## Slide 5: Certainty Equivalence Principle
Use pole-placement, tracking control and deterministic disturbance rejection controller synthesis methodology.
Estimate plant parameters using RLS PAA.
Controller parameters are re-calculated at every sample instance by assuming that the latest plant parameters estimates are the real parameters.

## Slide 6: Direct vs. Indirect Adaptive Control
Both use pole-placement, tracking control and deterministic disturbance rejection controller synthesis methodology.
Indirect adaptive control:
  Plant parameters are estimated using a RLS PAA.
  Controller parameters are calculated using the certainty equivalence principle.
  Use with plants that have non-minimum phase zeros. (Plant unstable zeros are not cancelled).
Direct adaptive control:
  Controller parameters are updated directly using a RLS PAA.
  Use with plants that do not have non-minimum phase zeros. (Plant zeros are cancelled).

## Slide 7: Outline
Review lecture 16: Pole-placement, tracking control and deterministic disturbance rejection for ARMA models.
Formulate the plant’s Parameter Adaptation Algorithm (PAA).
Implement an indirect adaptive controller, using the certainty equivalence principle.
For plants with minimum phase zeros, we will simplify the indirect adaptive controller.

## Slide 8: Deterministic SISO ARMA models
SISO ARMA model
Where all inputs and outputs are scalars:
control input
deterministic but unknown disturbance
output

## Slide 9: Deterministic SISO ARMA models
Where polynomials:
are co-prime and d is the known pure time delay

## Slide 10: Deterministic SISO ARMA models
We factor the zero polynomial as:
where
is anti-Schur
has the zeros that we
do not want to cancel

## Slide 11: Control Objectives
Pole Placement: The poles of the closed-loop system must be placed at specific locations in the complex plane.
Closed-loop polynomial:
Where:
cancelable plant zeros
anti-Schur polynomial of the form
chosen by the designer

## Slide 12: Control Objectives
Tracking: The output sequence must follow a reference sequence which is known
In general, yd(k) can be generated by a reference model of the form
The design of Am(q -1) and Bm(q -1) is not a part of this control design technique and these polynomials do not enter into the analysis
anti-Schur polynomial

## Slide 13: Control Objectives
Disturbance rejection: The closed-loop system must reject a class of persistent disturbances
Disturbance model:
Where
is a known annihilating polynomial
with zeros on the unit circle
are co-prime

## Slide 14: Control Law
Feedback and feedforward actions:
Feedforward action
(a-causal)
reference output

## Slide 15: Feedback Controller
Diophantine equation: Obtain polynomials
that satisfy:
Unstable plant zeros
Plant poles
Disturbance annihilating polynomial
Close loop
poles minus
cancelled zeros

## Slide 16: Feedback Controller

## Slide 17: Zero-phase error feedforward

## Slide 18: Outline
Review lecture 16: Pole-placement, tracking control and deterministic disturbance rejection for ARMA models.
Formulate the plant’s Parameter Adaptation Algorithm (PAA).
Implement an indirect adaptive controller, using the certainty equivalence principle.
For plants with minimum phase zeros, we will simplify the indirect adaptive controller.

## Slide 19: Certainty Equivalence Principle
Use pole-placement, tracking control and deterministic disturbance rejection controller synthesis methodology.
Estimate plant parameters using RLS PAA:
  Polynomial estimates:
Controller polynomials
Feedforward compensator
are computed using

## Slide 20: Parameter Adaptation Algorithm (PAA)
Use a series-parallel RLS algorithm to estimate plant parameters.
Pre-filter input u(k) and output y(k) using the disturbance annihilating polynomial, to prevent parameter biasing.
Use “parameter projection” to prevent unbounded control input

## Slide 21: PAA: sequence pre-filtering
Plant dynamics:
Disturbance:
Filtered input and output sequences:

## Slide 22: PAA: sequence pre-filtering
Multiply plant dynamics by annihilating polynomial:

## Slide 23: PAA: series parallel RLS
Filtered plant dynamics
Can be written as
Where:

## Slide 24: PAA: parameter projection
Assume that we know:
Minimum magnitude of DC gain of
Sign and minimum value of leading coefficient of

## Slide 25: Series parallel RL with projection
PAA:
A-priori parameter estimate (prior to projection)

## Slide 26: Series parallel RL with projection
PAA: Projection
Replace by if it becomes too small.

## Slide 27: Outline
Review lecture 16: Pole-placement, tracking control and deterministic disturbance rejection for ARMA models.
Formulate the plant’s Parameter Adaptation Algorithm (PAA).
Implement an indirect adaptive controller, using the certainty equivalence principle.
For plants with minimum phase zeros, we will simplify the indirect adaptive controller.

## Slide 28: Indirect Adaptive Controller
After each PAA iteration:
Update polynomials:
Factorize polynomial:
: has constant coefficient 1

## Slide 29: Indirect Adaptive Controller
Calculate controller polynomials:
by solving the Diophantine equation:
Plant parameter polynomial estimates are used
instead of actual polynomials

## Slide 30: Indirect Adaptive Controller
4) Calculate feedforward filter:
Where:
Replace by
if it becomes too small.

## Slide 31: Indirect Adaptive Controller
5) Calculate polynomial:
Notice that and
each have constant coefficient 1
Thus,
has constant coefficient

## Slide 32: Indirect Adaptive Controller
6) Adaptive control law is given by:

## Slide 33: Outline
Review lecture 16: Pole-placement, tracking control and deterministic disturbance rejection for ARMA models.
Formulate the plant’s Parameter Adaptation Algorithm (PAA).
Implement an indirect adaptive controller, using the certainty equivalence principle.
For plants with minimum phase zeros, we will simplify the indirect adaptive controller.

## Slide 34: Indirect Adaptive Controller with Stable Zeros
After each PAA iteration:
Update polynomials:
(no need to factorize )

## Slide 35: Indirect Adaptive Controller with Stable Zeros
2) Calculate controller polynomials:
by solving the Diophantine equation:
Plant parameter polynomial estimates are used
instead of actual polynomials

## Slide 36: Indirect Adaptive Controller with Stable Zeros
Feedforward filter is constant and known
Thus, there is no need to update it at every sample step.

## Slide 37: Indirect Adaptive Controller with Stable Zeros
3) Calculate polynomial:
Notice that both and have constant coefficient 1
Thus,
This coefficient is always

## Slide 38: Indirect Adaptive Controller with Stable Zeros
4) Adaptive control law is given by:
^
^