## Slide 1: ME 233 Advanced Control II Lecture 21 Parameter Convergence in Least Squares Estimation and Persistence of Excitation
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAA

## Slide 2: Estimation of ARMA model
Where
known bounded input
measured output

## Slide 3: Estimation of ARMA model
Where
Orders n and m are known
Relative degree d is known
a’s and b’s are unknown but constant coefficients
(anti-Schur)

## Slide 4: ARMA Model
Unknown parameter vector:
Known regressor vector:
n
m+ 1
n+m+1

## Slide 5: ARMA series-parallel estimation
A-priori output
A-priori error

## Slide 6: ARMA series-parallel estimation
A-priori error
Parameter error

## Slide 7: RLS Estimation Algorithm

## Slide 8: Overview
In Lecture 21 we learned how to analyze the stability of adaptive systems and proved:
  Convergence of the output error
Today we will provide conditions on the input sequence that guarantee that
also converges to zero.

## Slide 9: Parameter error convergence
Remember that
It can be shown that the n+m+1 parameter error also converges:
n
m+ 1

## Slide 10: Parameter error convergence
The steady-state parameter error satisfies
n
m+ 1
Regressor

## Slide 11: Parameter error convergence
The steady-state parameter error satisfies
Where the regressor correlation
is:

## Slide 12: Parameter error convergence
Since the steady-state parameter error satisfies
The regressor vector is persistently exciting if

## Slide 13: Persistence of Excitation
We need to find the conditions that the input sequence u(k) must satisfy to guarantee
that is persistently exciting.
Parameter
Adaptation
Algorithm
regressor
n
m+ 1

## Slide 14: Excitation matrix
Given and input sequence
Define the u-regressor of order n:
only present and past
values of u(k) are used

## Slide 15: Excitation matrix
Given and input sequence
Define the n x n excitation matrix:
Time average of

## Slide 16: Persistence of Excitation (PE)
The input sequence u(k)
is persistently exciting of order n if
the n x n excitation matrix is positive definite

## Slide 17: PE inputs in FIR models
is persistently exciting (PE) of order n iff
the following holds for all nonzero polynomials
of order at most n-1
Theorem:
where
w(k) is PE of order 1

## Slide 18: PE inputs in FIR models
Alternate statement of Theorem:
The following are equivalent:
u(k) is PE of order n
A(q -1)u(k) is PE of order 1 for all nonzero polynomials A(q -1) of degree at most n-1

## Slide 19: PE inputs in FIR models
Proof: Let
Then

## Slide 20: PE inputs in FIR models
Proof (cont’d):

## Slide 21: PE inputs in FIR models
Proof (cont’d):
Since U = aTCna, we see that U > 0,
if and only if .
Therefore, U > 0 for all nonzero polynomials A(q -1) of order at most n-1
if and only if

## Slide 22: PE inputs in FIR models
To determine the PE order of a sequence
Find a nonzero polynomial of order n such that A(q -1)u(k) is not PE of order 1
this means that is PE of order at most n
2. Compute the excitation matrix and verify that it is positive definite.

## Slide 23: Conditions for PE
u(k) is not PE of order 2
u(k) is PE of order 1
Examples: Constant input

## Slide 24: Conditions for PE in FIR Models
Examples: Sinusoid input
u(k) is not PE of order 3

## Slide 25: Conditions for PE in FIR Models
Examples: Sinusoid input

## Slide 26: Conditions for PE in FIR Models
Examples: Sinusoid input
u(k) is not PE of order 3
u(k) is PE of order 2

## Slide 27: Conditions for PE in FIR Models
Examples: Sum of Sinusoids

## Slide 28: Conditions for PE in FIR Models
Examples: Random process

## Slide 29: PE in Filtered Signals
Filtered signals:
Let
v(k) be the output of the model
A(q -1) is a nonzero polynomial of degree m < n

## Slide 30: PE in Filtered Signals
Filtered signals:
Let

## Slide 31: PE in Filtered Signals
Let v(k) be the output of the model
where A(q -1) is a nonzero polynomial
If u(k) is not PE of order n, then v(k) is not PE of order n
If u(k) is PE of order n and A(q -1) has degree m < n, then v(k) is PE of order n-m
If A(q -1) is anti-Schur, then u(k) is PE of order n if and only if v(k) is PE of order n
Theorem

## Slide 32: Interpretation of Theorem
Not PE of order n
Not PE of order n
PE of order n
PE of order n-m
order m<n

## Slide 33: Interpretation of Theorem
When A(q -1) anti-Schur
Not PE of order n
Not PE of order n
Not PE of order n
Not PE of order n
(this is redundant with part 1 of the theorem)

## Slide 34: PE in Filtered Signals
Preliminary result 1:
If u(k) is not PE of order 1, then v(k) is not PE of order 1
Proof:
Let

## Slide 35: PE in Filtered Signals
Proof of preliminary result 1 (continued):
Since u(k) is not PE of order 1, C1 = 0
The diagonal elements of Cn are zero
Since , this implies that Cn = 0
U = 0, which implies that v(k) is not PE of order 1

## Slide 36: PE in Filtered Signals
Preliminary result 2:
If A(q -1) is anti-Schur and v(k) is not PE of order 1,
then is not PE of order 1
The proof is based on frequency domain techniques for deterministic signals that are analogous to power spectral density techniques for wide sense stationary random signals
(see the additional material at the end of this lecture)

## Slide 37: PE in Filtered Signals
Proof of (1):
Let u(k) not be PE of order n
Choose nonzero B(q -1) of degree at most n-1 such that w(k) = B(q -1) u(k) is not PE of order 1
By the preliminary result, A(q -1) w(k) is not PE of order 1, which implies that B(q -1) v(k) is not PE of order 1
v(k) is not PE of order n

## Slide 38: PE in Filtered Signals
Proof of (2):
Let u(k) be PE of order n and A(q -1) have degree m < n
Suppose B(q -1)v(k) is not PE of order 1 where
B(q -1) has order at most n-m-1
B(q -1)A(q -1)u(k) is not PE of order 1
Since B(q -1)A(q -1) has order at most n-1 and u(k) is PE of order n, B(q -1)A(q -1) is the zero polynomial
Since A(q -1) is a nonzero polynomial,
B(q -1) is the zero polynomial
v(k) is PE of order n-m

## Slide 39: PE in Filtered Signals
Proof of (3):
By statement (1) of the theorem, if u(k) is not PE of order n, then v(k) is not PE of order n
It only remains to show that if v(k) is not PE of order n, then u(k) is not PE of order n
Let v(k) not be PE of order n and choose nonzero B(q -1) of order at most n-1 such that w(k)= B(q -1)v(k) is not PE of order 1
This implies that A(q -1)B(q -1)u(k) is not PE of order 1

## Slide 40: PE in Filtered Signals
Proof of (3), continued:
A(q -1)B(q -1)u(k) is not PE of order 1
Since A(q -1) is anti-Schur, we use preliminary result 2 to see that B(q -1)u(k) is not PE of order 1
Since B(q -1) is a nonzero polynomial
of order at most n-1
u(k) is not PE of order n

## Slide 41: ARMA Model (review)
Where
Orders n and m are known
Relative degree d is known
a’s and b’s are unknown but constant coefficients
(anti-Schur)

## Slide 42: ARMA Model (review)
Unknown parameter vector:
Known regressor vector:
n
m+ 1
n+m+1

## Slide 43: PE in ARMA models
Theorem:
Parameter estimates convergence to the true values

## Slide 44: PE in ARMA models - Proof
Simplifying assumption: the parameter error converges
Define: the LS output estimation error by
We know that

## Slide 45: PE in ARMA models - Proof
Notice that,
Therefore, if we can show that Cn+m+1 0, we will be able to conclude that

## Slide 46: PE in ARMA models - Proof
Notice that
where

## Slide 47: PE in ARMA models - Proof
From
We obtain

## Slide 48: PE in ARMA models - Proof
Polynomial of order n+m
Notice that since and

## Slide 49: PE in ARMA models - Proof
Polynomial of order n+m
Since e(k) = 0, it cannot be PE of order 1
Therefore,

## Slide 50: PE in ARMA models - Proof
So far, we know that if
then
where

## Slide 51: PE in ARMA models - Proof
This equation can be written as follows:
and:
where

## Slide 52: PE in ARMA models - Proof

## Slide 53: PE in ARMA models - Proof
Therefore, when
Parameter estimates convergence to the true values

## Slide 54: Example
Plant:
We need u(k) to be a PE sequence of order 4
to guarantee parameter convergence

## Slide 55: Example: Input Random Noise
u(k) : zero mean uniform white noise between [-1,1]
parameter convergence
a-priori error

## Slide 56: Example: Step Input
u(k) = 2*1(t)
a-priori error
NO parameter convergence

## Slide 57: Example: Sinusoidal input – 1 frequency
u(k) = 2*sin(t)
NO parameter convergence
a-priori error

## Slide 58: Example: Sinusoidal input – 2 frequencies
u(k) = 2*sin(t)+2cos(2*t)
parameter convergence
a-priori error

## Slide 59: Additional Material (you are not responsible for this)
Proof of preliminary result 2

## Slide 60: PE in Filtered Signals
Preliminary result 2:
If A(q -1) is anti-Schur and v(k) is not PE of order 1,
then is not PE of order 1
The proof is based on frequency domain techniques for deterministic signals that are analogous to power spectral density techniques for wide sense stationary random signals

## Slide 61: Stochastic and Deterministic Signals
WSS zero-mean random signals, X(k) and Y(k)
Deterministic signals, x(k) and y(k)
Average value of x(k+j)yT(k) over k

## Slide 62: Stochastic and Deterministic Signals
where G(z) is stable
WSS zero-mean random signals, U(k) and Y(k)
Deterministic signals, u(k) and y(k)
Scalar U(k) and Y(k)
Scalar u(k) and y(k)

## Slide 63: Proof of Preliminary Result 2
Let
A(q -1) be anti-Schur
v(k) not be PE of order 1
u(k) be generated by
Choose M such that
stable

## Slide 64: Proof of Preliminary Result 2
Therefore, we have

## Slide 65: Proof of Preliminary Result 2
v(k) not PE of order 1
u(k) not PE of order 1

## Slide 66: PE inputs
To determine the PE order of a sequence
Find an annihilating polynomial of order n such
this means that is at most PE of order n
Compute the excitation matrix
and verify that it is positive definite.

## Slide 67: Persistence of excitation for ARMA model identification
We need to find what conditions must the input sequence u(k) satisfy so that is persistently exciting.
Parameter
Adaptation
Algorithm
regressor
n
m+ 1

## Slide 68: PE in ARMA models
Given:
u(k) is bounded
is Schur
and are co-prime
n
m+ 1

## Slide 69: Derivation of Results
Determine conditions on the input sequence
For the parameter convergence of a Moving Average (MA) model
For the parameter convergence of an ARMA model

## Slide 70: Statistical Interpretation of LS Estimation
Stochastic Model
Where
observed output
zero-mean noise
regressor
unknown parameter vector

## Slide 71: Statistical Interpretation of LS Estimation
Assumptions:
zero-mean
Independence or orthogonality:
Ergodicity

## Slide 72: Statistical Interpretation of LS Estimation
Collect data for k observations:

## Slide 73: LS Statistical Interpretation
Collect data for k observations:
Where

## Slide 74: LS Statistical Interpretation

## Slide 75: Deterministic Least Squares Estimation
Parameter estimate after k observations:
Which minimizes the following cost functional:
Notice that is kept constant in the summation

## Slide 76: Deterministic Least Squares Estimation
: Parameter estimate which minimizes
Is given by the Normal Equation:

## Slide 77: LS Statistical Interpretation
Normal equation:
Stochastic model:
Parameter error vector:

## Slide 78: LS Statistical Interpretation
Substitute the stochastic model
Into the normal equation:
To obtain:

## Slide 79: LS Statistical Interpretation
Notice that
Therefore,

## Slide 80: LS Statistical Interpretation
Assume now that the parameter error converges:
Multiply by 1/k and take limits as

## Slide 81: LS Statistical Interpretation
By Ergodicity,

## Slide 82: LS Statistical Interpretation
If and are independent or orthogonal,
Since,

## Slide 83: LS Statistical Interpretation
The parameter error vector satisfies:
Thus, a sufficient condition for is that
(positive definite)

## Slide 84: LS Statistical Interpretation
We now define the Excitation matrix

## Slide 85: LS Statistical Interpretation
Theorem:
Under the conditions:
If the excitation matrix is positive definite,
the parameter error vector of the least square algorithm converges to zero.

## Slide 86: Persistence of Excitation (PE)
There exist finite constants:
Persistently exciting regressor:
For all k

## Slide 87: Persistence of Excitation (PE)
Persistently exciting regressor:
for all k
and a fixed m

## Slide 88: PE in Moving Average (MA) models
Finite Impulse Response (FIR) model:
where

## Slide 89: Conditions for PE in FIR Models
Persistently exciting input sequence:
Is persistently exciting (PE) of order n
if the regressor vector
is persistently exciting

## Slide 90: Conditions for PE in FIR Models
For a persistently exciting input sequence
with regressor
The excitation matrix Cn is a Positive Definite Toeplitz matrix